## Slide 1: Project Presentation
Daniele Sinigaglia (10574224)
Mattia Siriani (10571322)
Matteo Visotto (10608623)

## Slide 2: The project
Smart Buildings and Neighborhoods
Temperature and humidity sensors deployed in rooms of different neighborhood buildings
HVAC in the same room of a sensor activated by received data
Long term persistent data for analysis

## Slide 3: Technologies
Communication
Mosquitto MQTT Broker
IoT Motes Sensors
Contiki-NG
Backend flow
Node-Red
Apache Spark
Python
Statistics
Actuators

## Slide 4: Functionalities
Data sampling
Motes read and send temperature and humidity readings periodically
Data analysis
Data can be analyzed to retrieve different type of statistics
Data storage
Published data are stored permanently for further uses
Data on-demand
Data can be also read on-demand for live computation/use (ex. actuators)

## Slide 5: High level flow
6LowPan Network
RPL Border Router
TunSlip6
Local Mosquitto Broker
Cloud Mosquitto Broker
Node-Red
Data
Storage
Apache
Spark
tun0
Pub/Sub
Broker bridge
Pub/Sub
Write
Read
Actuators
Subscribe
POST
Notification

## Slide 6: Sensor State Machine

## Slide 7: Node-Red Flows
Sensor configurator
Data saving

## Slide 8: MQTT Topics
Base topic:
mtds/sensor/
Configuration topic:
config/{{sensor_id}}
Ex: mtds/sensor/config/mtdssens_0002
Publication topic:
data/A/B/C/D
Ex: mtds/sensor/data/A/0/S/1
Neighborhood
Building
Floor
Room
/
/
/
*Dividing location in topics is useful to subscribe for data with different granularity

## Slide 9: Spark analysis
Month of the year with the highest average night-day temperature difference, for each building.
Hourly, daily, and weekly moving average of each environmental quantity, at room, building, and
Neighborhood-scale.
Daily and night temperature difference at room and building-level.
1
2
3

## Slide 10: Actuators
Smart devices with full flagged operating system
Read sensor publication based on the location topic
Contains the logic to perform operations based on received data
Operations are simulated with a console print and a Telegram
notification
1
2
3
4

## Slide 11
DEMO TIME